## Slide 1: Omniverse Base Workshop 1 KUKA X IPI
2x 4h Course with examples to
  Learn the Basics in Omniverse, USD & Isaac Sim
  Enable you to do Robotic model preparation & Simulation
  Introduction to IsaacLab

## Slide 2: Trainer Introduction
Julian Zürn
Fabian Fichtl

## Slide 3: Institut für Produktion und Informatik
anwendungsorientierte Forschungseinrichtung
F&E-Projekte im Kontext Digitalisierung in der Produktion
Seit 2021 mit 30 Mitarbeitern
Technologietransfer und Startup Inkubator
VIBN und Industrial Metaverse in der Lehre
Technologietransferzentrum der Hochschule Kempten

## Slide 4: Introduction round
Please tell a few sentences about yourself, what you expect from this workshop and what you want to use Omniverse for

## Slide 5: Agenda Tag 1:
Introduction Metaverse
Omniverse basics: Nucleus | Data Formats | PhysX| extensions | Stage
5 min Pause
Hands on: Scene manipulation, Kinematics and Assets
  UI Manipulation Navigation, Manipulation (property window)
  Mass & Mesh manipulation
  First Robot
10 min Pause
Import and Tune a Robot
5 min Pause
First Robot Control (LULA test widget)
  Adding Sensors and Kameras
Notes: Timeline

## Slide 6: Agenda Tag 2:
Debugging Tools:
  Console, VS Code, UI
Scene Architecture
  Build your Scenario: Robot, Gripper, Controller, Environment, Handle Object
Pick & Place
Information Channels | Further Courses
Notes: Timeline

## Slide 7: Introduction to Omniverse

## Slide 8: Concept: Industrial Metaverse
Virtual Environment
Real-time Interaction and Collaboration
Purpose can span the Design, Simulation, Observation or Replay of arbitrary Objects and Processes in any Industry
The NVIDIA Omniverse platform is optimized to run 3D physics Simulations in real-time on NVIDIA RTX Hardware

## Slide 9: Omniverse Architecture

## Slide 10: Nucleus – The Omniverse Database
Enables Real-time Collaboration
Comprehensive User/Permission Management
Caching Mechanism for large Assets
Wide API and Script Integration
Enterprise Scalability
Overview — Omniverse Deployment
Notes: Gutes Bild, rechtlich nicht verwendbar: NVIDIA_Omniverse_Pipeline-1024x517.png (1024×517)
Enterprise Scalability (500 Concurrent Users, Up to 30 editing Users per Session, SSO and SSL Support)

## Slide 11: NVIDIA Isaac Ecosystem
IsaacLab (Open Source)
RL Assets and Environments
Tasking Framework
Domain Randomization and Terrain Generation
Imitation Learning
…
Omniverse
Physics
Rendering
UI
USD
Viewport
Isaac Sim (Closed Source)
Visual Coding (OmniGraph)
Robot Assembler
ROS
Synthetic Data Generation
URDF Compatibility
Isaac
Automator
Notes: Foundation of the Ecosystem is Omniverse, providing general capabilities
Isaac Sim builds upon this, providing robotics support and coding tools
Isaac Lab utilizes these capabilities to provide a state-of-the-art robotics learning framework
(With ist introduction, Isaac Lab deprecates the previous IsaacGymEnvs, OmniIsaacGymEnvs and Orbit frameworks)
All of this can be deployed in cloud infrastructures with the Isaac Automator
For managing multi-stage and multi-container setups NVIDIA provides OSMO (early access)

## Slide 12: Universal scene description
Notes: Für uns bedeutet usd ein einheitliches Datenformat das viele Formate ersetzen kann oder an bestehende Datenformate andocken kann und zusätzlich ermöglicht usd komplexe Szenen in einer skalierbarkeit auf der Omniverse Platform wie ich sie noch nicht kannte, bis heute nichts vergleichbares gesehen habe. Der Anfangsaufwand mit usd zu arbeiten gerade mit referenzing, kann anfangs gerade die Lernurve von Omnviverse stark versteilern, jedoch überwiegen später die Vorteile.
Die erwähnte

## Slide 13: Interacting with USD (in Omniverse scene)
UI Main Capabilities
  Viewport:
    Scene
  Property Window:
    Prim* Properties
  Omnigraph:
    Process Logic
    ROS Controller
  Various extensions
API Main Capabilities
  Python interface
  Robot Controllers
  URDF import
  Create the scene for IsaacLab
  Configure the policy
  Start training
*Nodes in the USD-scene tree are called Primitives or Prims

## Slide 14: Robot Data formats
 | URDF | SRDF | XRDF
Description Language | XML | XML | YAML
Purpose | Define Geometries and Kinematic Joints | Complements URDF Data with Semantic Grouping | Complements URDF Data with Kinematic Description
Collision Handling | Simple Shapes and Meshes | Collision Matrix (specifies handling for link pairs) | Collision Spheres along Robot Links
Joint Representation | Varying Types and Parameters | Defines Groups for Motion Planning | Advanced Configuration including Acceleration and Jerk Limits
Handling | Core Format in ROS and converted to USD upon import in Isaac Sim | ROS Moveit Assistant to generate Motion Plans | NVIDA CuMotion and Lula to generate Motion Plans

## Slide 15
Manual Modelling Phases Robot Simulation
Import URDF and convert to USD
Config Joint drives -> Test
Add Gripper/ Cameras
Add details to the stage of:
  URDF for ROS and RL
  SRDF for Moveit
  XRDF for Cumotion and LULA / RMPflow

## Slide 16: NVIDIA PhysX
The PhysX world comprises a collection of Scenes, each containing objects called Actors;
Each Scene defines its own reference frame encompassing all of space and time;
Actors in different Scenes do not interact with each other;
Characters and vehicles are complex specialized objects made from Actors;
Actors have a physical state: position and orientation, velocity or momentum, energy, etc;
Actor physical state may evolve over time due to applied forces, constraints such as joints or contacts, and interactions between Actors.

## Slide 17: Omniverse Stage

## Slide 18: 5 min Break
To be continued:
Practical session:
  Extensions installation
  Scene Manipulation
  Robot import + tuning
Until now:
We reviewed necessary Omniverse Basics and Resources

## Slide 19: Hands on!

## Slide 20: Getting started:
Start Omniverse Isaac Sim on the Machine
  Please give feedback if your application is loaded

## Slide 21: Standard Layout

## Slide 22: How-to: Viewport Navigation
Orbit: Left mouse btn. + ALT
Look: Right mouse btn. (RMB)
Fly/ Walk: Hold RMB; WASD / Q up / E down
Adjust Speed Hold RMB; Scroll
Jump to Selection: F

## Slide 23: Scene Prep tools (extensions)
Check for extensions:
  Action Graph
  URDF importer

## Slide 24: How-to: Add Physics Scene
Create a Physics Scene
Create a ground plane

## Slide 25: Asset Store
Import a Box
  Move above ground plane
  Adjust the size
  Add (Rigid Body and and Collider)
  Press Play to start the Simulation
How-to↓
Notes: Compare Viewport with property changes

## Slide 26: How-to: Use Asset Store
1
2
a
b
Search
Drag & Drop (to Stage or Viewport)
Notes: 11

## Slide 27: How-to: Manipulation in Viewport
Move Selection* (W)
Rotate Selection* (E)
Scale Selection (R)
Snap Selection* (S)
Update Attributes with value
*RMB on icon shows further options

## Slide 28: How-to: Add Rigid-body & Collider
Select cracker box XForm in Stage Tree
Use Context menu on box

## Slide 29: Asset Store
Import a Box
  Move above ground plane
  Adjust the size
  Add (Rigid Body and and Collider)
  Press Play to start the Simulation
How-to↑
Notes: Compare Viewport with property changes

## Slide 30: Assemble the first self-built Robot
Stop the Simulation
Create Cylinders
  Move/ orient to the side
  Create a revolute joint
  Add Angular drive
  Modify target velocity + stiffness
Start the Simulation
How-to↓

## Slide 31: How-to: Add Cylinder
Ensure World is selected in Stage
Use Context menu in Viewport or Stage
3. Adjust scaling and orientation to represent a wheel
4. Add Rigid Body & Collider
5. Use Ctrl+C and Ctrl+V to replicate the wheel
6. Move the wheels to reasonable positions around the box

## Slide 32: How-to: Add Joint
Holding Ctrl, select the box then the cylinder
Create joint using the context menu
Repeat for all wheels

## Slide 33: How-to: Adjust Joint and Add Drive
Filter for Joints
Select all joints (via Shift or Ctrl)
Adjust joint rotation
Add Drives to joints (via Context menu)

## Slide 34: How-to: Adjust Drive
Set a Velocity(~20-100)
Iterate:
  Set Damping & Stiffness Values
  Restart Simulation for Testing*
*Not restarting the simulation leads to misleading results due to the forces that already applied before the update

## Slide 35: Assemble the first self-built Robot
Stop the Simulation
Create Cylinders
  Move/ orient to the side
  Create a revolute joint
  Add Angular drive
  Modify target velocity + stiffness
Start the Simulation
How-to↑

## Slide 36: Rigid Bodies and Colliders
Simpler approximation = faster Simulation

## Slide 37: Robot assembly
Structure of mobile / static robot
  Articulation chain
  root link free / fixed
Link 1
Base Link Articulation root
Link 2
Link 3
Link n
No Base Link

## Slide 38: Joint types and properties

## Slide 39: Joints
Notes: Nicht ins detail gehen

## Slide 40: Joint types and properties
Joint drives are internally simulated with PD-Controllers
Stiffness property <-> Proportional coefficient
Damping property <-> Derivative coefficient
⚠This can lead to unexpected behavior at low simulation frequencies

## Slide 41: 10 min Break
To be continued:
Practical session:
  Robot import + tuning
Until now:
We reviewed necessary Omniverse Basics and Resources
Practical session:
  Extensions installation
  Scene Manipulation

## Slide 42: How-to: Starting with a real Robot
Open File->import
Navigate to a URDF File
Modify the Options
  Verify Model and Links
  Adjust Joints & Drives
  Verify Colliders
Click Import
How-to↓

## Slide 43: Robot import Tools
LULA URDF Import Tool:
  Import Robot URDF
  Start scene -> look at joint drives
Physics Inspector Tool:
  Activate scene
  Choose IISY to inspect-> control joint limits/ direction
Gain tuner:
  Adjust Stiffness & Damping and test the parameters
Preparation of self and external collision shape:
  Sphere approximation Collider tool for RMP

## Slide 44: Robot Description Editor

## Slide 45: Sphere Approximation Result

## Slide 46: Lula Test Widget

## Slide 47: Lula Test Widget

## Slide 48: Sensors
Adding a Wrist Camera to the Robot
  Tune the Camera

## Slide 49: End of Day 1
For further questions mail us:
fabian.fichtl@hs-kempten.de
julian.zuern@hs-kempten.de
Please provide some Feedback Verbal or via:

## Slide 50: Omniverse Base Workshop 1 KUKA X IPI
2x 4h Course with examples to
  Learn the Basics in Omniverse, USD & Isaac Sim
  Enable you to do Robotic model preparation & Simulation
  Introduction to IsaacLab

## Slide 51: Review of Day 1
We reviewed necessary Omniverse Basics and Resources
Practical session:
  Extensions installation
  Scene Manipulation
  Robot import + tuning

## Slide 52: Agenda Tag 2:
Scene Architecture
  Build your Scenario: Robot, Gripper, Controller, Environment
Debugging Tools:
  Console, VS Code, UI
Materials
Motion Planning & Motion Learning
Practical Session: Pick & Place
Information Channels | Further Courses
Notes: Timeline

## Slide 53: Interacting with USD (in Omniverse scene)
UI Main Capabilities
  Viewport:
    Scene
  Property Window:
    Prim* Properties
  Omnigraph:
    Process Logic
    ROS Controller
  Various extensions
API Main Capabilities
  Python interface
  Robot Controllers
  URDF import
  Create the scene for IsaacLab
  Configure the policy
  Start training
*Nodes in the USD-scene tree are called Primitives or Prims

## Slide 54: Scene Assembly
Payload: blue ↔ Reference: orange
  The user can choose to not load a payload
  References always get loaded
  I = Instancing active
How to build a reference scene architecture
  To test different robots/ grippers
  Test Script of Robot Assembly
Repository (Asset store/ Local)
Robot.usd
Gripper.usd
Scene/Objects.usd
Scene
Built from References

## Slide 55: Assemble Your Scene
How-to↓

## Slide 56: TODO click-anleitungen
Open environment template & inspect it✅
Drag robot into Viewport or Stage✅
Add ROS Controller✅
Inspect ROS2 subscriber ActionGraph
Run scene
Execute ROS2 script (from VS code) -> ToBeCreated
⚠

## Slide 57: How-to: Add the Environment
1. Drag USD scene from content browser onto Stage tree

## Slide 58: How-to: Add the Robot
1. Drag robot from content browser onto Stage tree

## Slide 59: How-to: Add the Controller
Open Graph Assistant
Check Configuration and press ok

## Slide 60: How-to: View the Controller
Use Context menu in Stage
Use Visual Scripting Layout (Ctrl+6 -> ‘Edit Graph’)
or

## Slide 61: Assemble Your Scene
How-to↑

## Slide 62: Save Scene
Use the USDA format
Inspect the structure and payloads

## Slide 63: Debugging Tools
creates
If you open .py in OV, the VS Code Link dependencies are created automatically -> Enables hot reload of code
https://docs.omniverse.nvidia.com/extensions/latest/ext_vs-code-link.html

## Slide 64: Debugging Tools
Helpful to reuse example code or look into USDA file

## Slide 65: Debugging Tools
Script Editor

## Slide 66: Manipulate the Scene by Python API
Open the Script Editor
  Open the file scene_Manipulation.py.
  Run it
  Try to create another prim for example a cone:
import omni.usd import omni.kit.commands from pxr import Gf
# Get current stage
stage = omni.usd.get_context().get_stage()
# Create cube with specified parameters
result, prim_path = omni.kit.commands.execute(
"CreateMeshPrim",
prim_type="Cube",
prim_path="/World/Cube",
object_origin=Gf.Vec3f(0, 0, 0),
half_scale=50.0,
u_verts_scale=1,
v_verts_scale=1,
w_verts_scale=1 )
# Create cone with specified parameters
result, prim_path = omni.kit.commands.execute(
"CreateMeshPrim",
prim_type=" Cone",
prim_path="/World/Cone",
object_origin=Gf.Vec3f(0, 0, 0),
half_scale=50.0,# 1m Height/Diameter (dep. on def.)
u_verts_scale=1,
v_verts_scale=1,
w_verts_scale=1 )

## Slide 67: Documentation
$ cd isaacsim/docs
$ python3 -m http.server 9999
https://docs.isaacsim.omniverse.nvidia.com/4.5.0/py/index.html
Online or Local (latter might not be available)
Notes: Your best friend

## Slide 68: Referencing Prims
Create new scene through GUI
Open Script Editor
Open File assemble_scene.py
Analyze Content…
Run Script
Notes: TODO
- Prepare
- Idea -> Force use of debugging tools

## Slide 69: Materials & physics Materials
Materials:
Color Map
Reflectivity
Absorption
Many others and mixtures/ Shaders
Physics Materials:
Static Friction
Dynamic Friction
Restitution
Density

## Slide 70: 10 min Break
To be continued:
Motion Planning & Motion Learning
Practical Session: Pick & Place
Until now:
Scene Architecture
  Build your Scenario: Robot, Gripper, Controller, Environment
Debugging Tools:
  Console, VS Code, UI
Materials

## Slide 71: Motion Planning Libraries
Lula
  Kinematics Solver (fast-forward and inverse kinematics)
  Trajectory Generator (using one or more planners)
  Global Planners (e.g. RRT-Connect, JT-RRT)
  Local Planners (e.g. RMPflow)
  CPU-based
CuMotion
  Similar capabilities as Lula
  Supports real-time control
  Builds upon CuRobo (CUDA-accelerated)
RRT…Randomly-Exploring Random Tree
RMP… Riemannian Motion Policies
⚠Lula algorithms require a robot_description.yaml. It contains active and fixed joints, default joint positions, collision spheres and more. This format will be superseded by the XRDF-format.

## Slide 72: Prerequisites for CuMotion with RMP
An URDF file, used for specifying robot kinematics as well as joint and link names. Position limits for each joint are also required.
An (X)RDF file which can be generated using the Lula Robot Description Editor UI tool. (configure drives, robot density and collision meshes)
A RMPflow configuration file in YAML format, containing parameters for all enabled RMPs.*
*For algorithms other than RMPflow different configurations and are required
Notes: URDF extra: Other properties in the URDF are ignored and may be omitted; these include masses, moments of inertia, visual and collision meshes, etc.

## Slide 73
Notes: XML Reference - MuJoCo Documentation

## Slide 74: IsaacLab Workflow – High Level
Design & Tune
Robot
  Isaac Sim
  Import URDF/ Run Script
  Optimize Kinematics
  Generate Synthetic Data
Train Robot
  Isaac Lab
  Define Task Workflow
  Support for 4 RL Libraries: RL-Games, RSL RL, SKRL, SB3
Deploy Robot
  Isaac Sim
  e.g. Running on ROS

## Slide 75
Notes: [example Isaac Lab environments]

## Slide 76: Task Workflows in IsaacLab
Direct RL Workflow
Manager-based RL Workflow
Notes: Direct: The user defines a single class that implements the entire environment directly. This class is responsible for computing observations, applying actions, and computing rewards.
Manager-based: The environment is decomposed into individual components (or managers) that handle different aspects of the environment (such as computing observations, applying actions, and applying randomization). The user defines configuration classes for each component and the environment is responsible for coordinating the managers and calling their functions.
This manager-based workflow is more modular and allows different components of the environment to be swapped out easily. This is useful when prototyping the environment and experimenting with different configurations.
On the other hand, the direct workflow is more efficient and allows for more fine-grained control over the environment logic as well as the utilization of optimized frameworks such as PyTorch JIT or Warp. This is useful when optimizing the environment for performance or when implementing complex logic that is difficult to decompose into separate components.

## Slide 77: Integrating ML Models
Training models on synthetic data generated in Isaac Sim or COSMOS
Foundation model as perception or reasoning module within the Isaac Lab workflow
Isaac Lab RL policy optimization
Groot N1:
  Requires Trajectory Data, Video
  https://github.com/NVIDIA/Isaac-GR00T/blob/main/media/model-architecture.png
π0.5
  Sensory Data
  https://pi.website/blog/pi05
OCTO
  Generalist Robotic Policy
  🐙 Octo: An Open-Source Generalist Robot Policy

## Slide 78: How to generate Trajectory Data
Classic: Real Robot „imitation learning“
Trajectory generators
Applied RL policies
Teaching sim. Robot with imitation learning

## Slide 79: Assemble a gripper to your robot
UI:
  The Tool joins two articulation trees to one. Guides you how
Python API Code is created automatically from the UI. This can be reused for later automatically create a stage + assembly

## Slide 80: 5 min Break
To be continued:
Practical Session: Pick & Place
Movie Capture
Until now:
Scene Architecture
Build your Scenario: Robot, Gripper, Controller, Environment
Debugging Tools:
  Console, VS Code, UI
Materials
Motion Planning & Motion Learning

## Slide 81: Pick & Place Setup
Create new Scene
Add a robot from the workshop material:
  Content -> Workshop -> Robots -> IISY 15_Suction
Add graph logic/controller
Start script assemble_pick_place.py
  -> Start the scene by hitting play
https://docs.omniverse.nvidia.com/isaacsim/latest/advanced_tutorials/tutorial_advanced_omnigraph_pickplace_controller.html
⚠

## Slide 82: Pick & Place Phases
Phase 0: Move above the cube center at the ‘end_effector_initial_height’.
Phase 1: Move ee down to encircle the target cube
Phase 2: Wait for Robot’s inertia to settle.
Phase 3: Close grip.
Phase 4: Move ee up again, keeping the grip tight (lifting the block).
Phase 5: Move the ee toward the goal xy, keeping the height constant.
Phase 6: Move ee vertically toward goal height at the ‘end_effector_initial_height’.
Phase 7: Loosen the grip.
Phase 8: Move ee up again at the ‘end_effector_initial_height’
Phase 9: Move ee towards the old xy position.
ee... end_effector

## Slide 83: Movie Capture Tool
Navigate to Window -> Extensions Manager using the top-level menu
Search Movie Capture in the text field, to reveal the omni.kit.window.movie_maker.
Click the toggle to enable the extension.
Open the extension in rendering -> Movie Capture

## Slide 84: Movie Capture + simple Animation

## Slide 85: Feedback Workshop
For further questions mail us:
fabian.fichtl@hs-kempten.de
julian.zuern@hs-kempten.de

## Slide 86: Ressources & further Courses

## Slide 87: Omniverse Glossary
Omniverse Glossary of Terms — Omniverse Developer Workstations

## Slide 88: USD
Payload vs Reference: https://forums.developer.nvidia.com/t/usd-payload-vs-reference-vs/252658

## Slide 89
Joints
https://nvidia-omniverse.github.io/PhysX/physx/5.3.0/_downloads/6acf3afb8f69452757e0e766b5a22978/implicitDrives.pdf

## Slide 90: URDF Import
https://docs.isaacsim.omniverse.nvidia.com/4.5.0/robot_setup/ext_isaacsim_asset_importer_urdf.html

## Slide 91: Gripper
https://docs.isaacsim.omniverse.nvidia.com/latest/robot_setup/assemble_robots.html
https://docs.isaacsim.omniverse.nvidia.com/latest/robot_simulation/ext_isaacsim_robot_surface_gripper.html
cobotta demo und anschließend mit iisy
https://docs.isaacsim.omniverse.nvidia.com/latest/robot_setup/import_manipulator.html
https://docs.isaacsim.omniverse.nvidia.com/latest/manipulators/manipulators_configure_rmpflow_denso.html#isaac-sim-app-tutorial-configure-rmpflow-denso
https://docs.isaacsim.omniverse.nvidia.com/latest/robot_setup/grasp_editor.html

## Slide 92: Roboter konfiguration
https://docs.omniverse.nvidia.com/isaacsim/latest/advanced_tutorials/tutorial_configure_rmpflow_denso.html
Articulation Root -> Mobil oder stationär
https://docs.omniverse.nvidia.com/extensions/latest/ext_physics/articulations.html

## Slide 93: Inverse Kinematics solver
https://isaac-sim.github.io/IsaacLab/main/source/tutorials/05_controllers/run_diff_ik.html

## Slide 94: MoveIt
https://moveit.picknik.ai/main/index.html
https://moveit.picknik.ai/main/doc/concepts/concepts.html

## Slide 95: Cumotion
https://nvidia-isaac-ros.github.io/concepts/manipulation/index.html#nvidia-cumotion
Isaac Manipulator consists of a set of components and reference workflows for advanced perception-driven manipulation. These components include state-of-the-art packages for object detection and object pose estimation, as well as obstacle-aware motion generation.

## Slide 96: Task Space Controller
https://isaac-sim.github.io/IsaacLab/main/source/tutorials/05_controllers/run_diff_ik.html

## Slide 97: Self paced Courses:
https://learn.nvidia.com/courses/course?course_id=course-v1:DLI+S-OV-31+V1&unit=block-v1:DLI+S-OV-31+V1+type@vertical+block@bd7da7c3339a42c69f073ca845778391
https://learn.nvidia.com/courses/course-detail?course_id=course-v1:DLI+S-OV-31+V1
https://learn.nvidia.com/courses/course-detail?course_id=course-v1:DLI+S-OV-15+V1
https://learn.nvidia.com/courses/course-detail?course_id=course-v1:DLI+S-OV-27+V1
https://learn.nvidia.com/courses/course-detail?course_id=course-v1:DLI+S-OV-29+V1
https://learn.nvidia.com/courses/course-detail?course_id=course-v1:DLI+S-OV-20+V1
https://learn.nvidia.com/courses/course-detail?course_id=course-v1:DLI+S-OV-28+V1
https://academy.nvidia.com/en/course/nvidia-ai-enterprise-administration/?cm=55144